## Slide 1: Update on Measurements and Simulations at Cambridge: SKALA element + LNA
Eloy de Lera Acedo
Nima Razavi Ghods
Cavendish Laboratory
University of Cambridge
Cambridge, UK.

## Slide 2: Overview
Design and Simulations
Measurements
  Impedance and coupling (AAVS0 array)
  Pattern
  LNA
Future work and conclusions
  SKALA with integrated ground plane
  Cross-polarization

## Slide 3: Design
Dual-polarization from (50) 70-450 (600) MHz
Element gain ~ 7dB
Receiver noise < 35 K above 100 MHz
Receiver gain > 36 dB (2 stages)

## Slide 4: Design and Simulations
The antenna was designed using CST
The simulations of the element were confirmed using HFSS
The MoM/MBF specialized code (UCL/UCAM) was used to verify the behaviour at array level (SKA stations)
  Mutual coupling analysis (averages out for random configurations)
  Low order models for calibration
  Objective of the measurement campaign with single elements and the AAVS0 array: Confirm that these simulations are correct. We design the SKA with simulations!

## Slide 5
EM characterization of SKA arrays
  Mutual coupling effects randomize out in quasi-random configurations.**
*Gonzalez-Ovejero, D., De Lera Acedo, E., Razavi-Ghods, N., and Craeye, C. (2009)
*Gonzalez-Ovejero, D., De Lera Acedo, E., Razavi-Ghods, N., Garcia, E., and Craeye, C. (2011)

## Slide 6
EM characterization of SKA arrays
  Accurate EM simulations can be useful for the telescope calibration.**
*De Lera Acedo, E., Razavi-Ghods, N., Gonzalez-Ovejero, D., Sarkis, R., and Craeye, C. (2011)
**Craeye, C., Gonzalez-Ovejero, D., Razavi-Ghods, N., and de Lera Acedo, E. (2012)
+
Q=3
=

## Slide 7
EM characterization of SKA arrays
  The method has been tested before.*
*Raucy, C., De Lera Acedo, E., Craeye, C., Gonzalez-Ovejero, D., and Razavi-Ghods, N. (2012)
Measurements
Simulations MoM
Simulations MBF

## Slide 8
EM characterization of SKA arrays:
Antenna model in simulations
CST
MoM
spine

## Slide 9: Design and Simulations
  Important for a SKA antenna element (embedded in a station)
Calibratability
Sensitivity
Effective aperture
Noise
(sky, ground, LNA)
Pattern
Antenna
impedance
LNA noise & gain
LNA intermodulation
Cost (including deployment and durability)
Cross-polarization
Element’s footprint
Material properties
Materials, construction, assembly, maintenance, etc.
Power consumption
LNA power consumption
Linearity, stability, ripple

## Slide 10: Design and Simulations
  Sensitivity (“Antenna Standardization report”: Shantanu Padhi, Ver: 2.0, 1 August 2012)
~1,300 m^2/K for 500,000 elements

## Slide 11: Measurements
  We can measure most of what we can simulate
  *See more about future measurements in Nima’s talk (test plan)
Calibratability
Sensitivity
Effective aperture
Noise
(sky, ground, LNA)
Pattern
Antenna
impedance
LNA noise & gain
LNA intermodulation
Cost (including deployment and durability)
Cross-polarization
Element’s footprint
Material properties
Materials, construction, assembly, maintenance, etc.
Power consumption
LNA power consumption
Linearity, stability, ripple

## Slide 12: Measurements: Impedance and coupling tests
  Scaled prototype
+
-
1
2
VNA
Zdiff

## Slide 13: Measurements: Impedance and coupling tests
  SKALA element
CST
MoM
Test board

## Slide 14: Measurements: Impedance and coupling tests
SKALA element

## Slide 15: Measurements: Impedance and coupling tests
*B. Fiorelli

## Slide 16: Measurements: Impedance and coupling tests
2 SKALA elements 1.5 m apart
  AAVS0 array

## Slide 17: Measurements: Impedance and coupling tests
TOP VIEW
1.5 m

## Slide 18: Measurements: Impedance and coupling tests
  Common-mode currents (with Howard Reader – April 2012)

## Slide 19: Measurements: Impedance and coupling tests

## Slide 20: Measurements: Impedance and coupling tests

## Slide 21: Measurements: Impedance and coupling tests

## Slide 22: Measurements: Pattern
  Scaled prototype:
    Direct line of sight range (main reflected ray absorbed).
    Using Spectrum analyser, signal generator and power combiner.
    At Lords Bridge. Easy, quick and great results.

## Slide 23: Measurements: Pattern

## Slide 24: Measurements: Pattern
  SKALA element (at QinetiQ)
    Arch above antenna (near field).
    Ground refection range.

## Slide 25: Measurements: Pattern

## Slide 26: Measurements: Pattern
70 MHz | 200 MHz
300 MHz | 450 MHz
E-plane cut

## Slide 27: Measurements: Pattern
300 MHz | 450 MHz
H-plane cut
200 MHz

## Slide 28: Measurements: Pattern
  SKALA element (with Howard Reader)
    At Stellenbosch University.
    Ground refection range.
www.paardefontein.co.za

## Slide 29: Measurements: Pattern
  Near field pattern measurement (AAVS0)

## Slide 30: Measurements: LNA
  Concept
COAX
LNA1
LNA2

## Slide 31: LNA
  Design
AVAGO
MGA-16516
2nd stage
amplifier
Transformer

## Slide 32: LNA
  Simulations

## Slide 33: Measurements: LNA
  Gain

## Slide 34: Measurements: LNA
  Hot/cold measurement with 150 Ω load.
    Liquid Nitrogen (77 K)
    Room temperature (290 K)
    Filtering

## Slide 35: Measurements: LNA
  1st stage amplifier with Agilent noise analyser in reverberation chamber.

## Slide 36: Measurements: LNA
  Noise tuner and noise parameter measurement in reverberation chamber at ASTRON.

## Slide 37: Measurements: LNA
  Intermodulation
    Not great expectations (by design):
      OIP2: 17 dBm
      OIP3: 19 dBm
  Others:
    Tests on single transistors.
    Connection to antenna and noise measurement in reverberation chamber.
    RFI monitoring.

## Slide 38: Future work and conclusions
  SKALA with integrated ground plane

## Slide 39: Future work and conclusions
  Cross-polarization (“IXR SKALA with GP vs Vivaldi V2 with Soil C”, 08/10/2012 – B. Fiorelli)

## Slide 40: Future work and conclusions
  Most measurements already done.
  The performance is looking like the simulations said.
    Element
    LNA
  More measurements to be done, using a back-end (see Nima’s talk).
  More development coming.
    Even cheaper element, long lasting materials, integrated ground plane.
    Lower power consumption for LNA, better IP2/3.

## Slide 41
Lord’s Bridge Observatory
SKALA-AAVS0

## Slide 42
Thank you! Any questions?