## Slide 1: RF over fibre
Federico Perini
AA-low Technical Progress Meeting
Medicina, 22-23 September 2012

## Slide 2: RoF concept
STaN CoDR Jodrell Bank
28th‐30th June 2011

## Slide 3: RoF concept
200-500m link length

## Slide 4: Signal Transportation & RX chain
 -100dBm Input Power
(noise at the antenna level)  70dB min Gain
LNA
RF Amp
Copper
or
RoF link
Antenna
RF Amp
ADC
Receiver
Tsys AAlo
Tsky
Trec AAlo
SFDRRXchain=(OIP3-G+KT-NF)=(35-71+174-0.5)= =91.7dB/Hz2/3

## Slide 5: Copper link
Freq | Att. | Attenuation vs Length[dB] |  |  | 
[MHz] | [dB/m] | 50m | 100m | 200m | 500m
50 | 0.041 | 2.05 | 4.1 | 8.2 | 20.5
100 | 0.056 | 2.8 | 5.6 | 11.2 | 28
200 | 0.082 | 4.1 | 8.2 | 16.4 | 41
400 | 0.118 | 5.9 | 11.8 | 23.6 | 59
Freq | Att. | Attenuation vs Length[dB] |  |  | 
[MHz] | [dB/m] | 50m | 100m | 200m | 500m
500 | 0.45 | 22.5 | 45 | 90 | 225
LOFAR Coax Cable (75Ohm/TV)
2-PAD Twisted Cable (CAT-7)
SFDRRXchain=91.6dB/Hz2/3

## Slide 6: Copper link
Freq | Att. | Attenuation vs Length[dB] |  |  | 
[MHz] | [dB/m] | 50m | 100m | 200m | 500m
50 | 0.029 | 1.45 | 2.9 | 5.8 | 14.5
150 | 0.050 | 2.5 | 5 | 10 | 25
220 | 0.061 | 3.05 | 6.1 | 12.2 | 30.5
450 | 0.089 | 4.45 | 8.9 | 17.8 | 44.5
HDF400 Coax Cable (50Ohm/WiFi)
SFDRRXchain=91.6dB/Hz2/3

## Slide 7: RoF link (BEST-2)
Gain (dB) | -25
Gain Flatness (dB) | +/-0.75
IRL (dB) | >15
ORL (dB) | >20
IIP3 (dBm) | +33
NF (dB) | 36
SFDR (dB/Hz2/3) | 120
1.3um DFB SLT4260
from Sumitomo

## Slide 8: RoF link (BEST-2)
SFDRRXchain = 91dB/Hz2/3

## Slide 9: Cost reduction?
1.3um DFB SLT4260
from Sumitomo
SMA RFin
PCB fixture
SMB for DC power
(to Laser Driver)
Passive
Matching Network
RF choke

## Slide 10: Cost reduction?
SFDRDFB_Link = 118dB/Hz2/3

## Slide 11: Not only cost…
Vcc (V) | If (mA) | P (mW)
6 | 3 | 18
 | 5 | 30
 | 10 | 60
 | 15 | 90
 | 20 | 120
 | 25 | 150
 | 30 | 180
 | 35 | 210
 | 50 | 300

## Slide 12: VCSEL, VCSEL, VCSEL…
Through the collaboration with CNR – IEIIT (Turin):
1.25, 2.5, 4.5 and 10Gbps COTS devices:

## Slide 13: Measurement path
L-I
Curve
P1dB
S
NF
IP3
SFDR
Passive
Match
Laser
PD
Passive
Match
RFin
RFout
Optical
fibre

## Slide 14
VERTILAS 1300nm

## Slide 15
VERTILAS 1300nm
SFDRVertilas_Link = 110dB/Hz2/3

## Slide 16
VIS 850nm

## Slide 17
VIS 850nm
NO OPTOISOLATOR?

## Slide 18
Optowell 850nm

## Slide 19
Optowell 850nm
NO OPTOISOLATOR?

## Slide 20
VCSEL characterisation
Good experience gained in devices characterization
  Link with UNIBO open (see next slides)
  Found first suitable device (Vertilas)?
Instrumentation for 1300nm devices quite good
Lack of instrumentation and accessories for 850nm devices
  new photodetector acquired
  new optical power meter acquired
  optoisolator under evaluation

## Slide 21
Current and future work
Passive
Match
Laser
PD
Passive
Match
RFin
RFout
Optical
fibre
Laser driver
TIA
A lot of VCSEL still to be tested
Searching of low cost DFB should goes in parallel

## Slide 22: Optics Laboratory of DEI – UniBO Radio over Fiber research activities
Department of Electrical, Electronic and Information Enginnering (DEI) “Guglielmo Marconi”
Responsible: Prof. Giovanni Tartarini
More than 10 years of experience in the
Radio over Fiber technology.
Active collaboration with R&D sector of private companies
Participation to National and European Research Projects
    Integration of Wide Band Services (InSeBaLa, Italy, 2004-2006)
    Architectures for Flexible Photonic Home and Access Networks
    (ALPHA, EU FP7, 2008-2011)

## Slide 23: Optics Laboratory of DEI – UniBO Radio over Fiber research activities
Department of Electrical, Electronic and Information Enginnering (DEI) “Guglielmo Marconi”
Theoretical Analysis and Modelling
  Locally developed software (MATLAB , Simulink®, ….)
  Commercial tools (OptSim, Comsol Multiphysics,…)
Experimental investigations
  Automated measurement benches (LabVIEW)
  State-of-the-art equipment, which include:
    Three-port Vector Network Analyzer (10 MHz-9 GHz)
    Optical Spectrum Analyzer (600 - 1750 nm, 62.5/125 input, Res. 70 pm)
    Vector Signal Analyzer (9 kHz-6 GHz, Analysis band 31.25 MHz)
    Vector signal generator (9 kHz-6 GHz, Modulation band 120 MHz)
    Laser driver (200/500mA source current range)

## Slide 24: List of Journal papers on the topic
D. Visani, M. N. Petersen, F. Sorci, P. Faccin, G. Tartarini,
“In-building Wireless Distribution in legacy Multimode Fiber with an improved RoMMF system,”
IEEE Microwave and Wireless Components Letters, article in press, 2012
G. Alcaro, D. Visani, L. Tarlazzi, P. Faccin, G. Tartarini,
“Distortion Mechanisms Originating from Modal Noise in Radio over Multimode Fiber Links,”
IEEE Transactions on Microwave Theory and Techniques, vol. 60, no. 1, pp. 185-194, Jan. 2012.
D. Visani, G. Tartarini, P. Faccin, L. Tarlazzi,
“Cost-effective radio over fiber system for multi service wireless signal,”
Optics Communications, vol. 284, no. 12, pp. 2751-2754, June 2011.
M. N. Petersen, G. Tartarini, D. Visani, P. Faccin, L. Tarlazzi,
“Influence of transmitter chirp and receiver imperfections on RF gain in short-range ROMMF systems,”
Microwave and Optical Technology Letters, vol. 53, no. 4, pp. 822-824, Apr. 2011.
D. Visani, G. Tartarini, M. N. Petersen, L. Tarlazzi, P. Faccin,
“Link Design Rules for Cost-Effective Short-Range Radio Over Multimode Fiber Systems,”
IEEE Transactions on Microwave Theory and Techniques, vol. 58, no. 11, pp. 3144-3153, Nov. 2010.
D. Visani, G. Tartarini, M. N. Petersen, P. Faccin, L. Tarlazzi,
“Effects of laser frequency chirp on modal noise in short-range radio over multimode fiber links,”
OSA Applied Optics, vol. 49, no. 6, pp. 1032-1040, Feb. 2010.
D. Visani, G. Tartarini, L. Tarlazzi, P. Faccin,
“Transmission of UMTS and WIMAX Signals Over Cost-Effective Radio Over Fiber Systems,”
IEEE Microwave and Wireless Components Letters, vol. 19, no. 12, pp. 831-833, Dec. 2009.
G.Tartarini, A.Lena, D. Passaro, L. Rosa, S. Selleri, P. Faccin, E. Fabbri.
“Harmonic and Intermodulation Distortion Modeling in IM-DD Multi-Band Radio over Fiber Links exploiting Injection Locked Lasers” .
Optical and Quantum Electronics vol. 38, pp. 869 - 876., 2006
G. Tartarini, P. Faccin,
“Efficient characterization of harmonic and intermodulation distortion effects in dispersive radio over fiber systems with direct laser modulation,”
Microwave and Optical Technology Letters, vol. 46, pp. 114 – 117, 2005.

## Slide 25: List of Conference Papers on the topic
D. Visani, F. Sorci, P. Faccin, G. Tartarini,
“Comeback of Fabry-Perot RoMMF Transmitters for Improve LTE Signal Distribution”,
IEEE International Topical Meeting on Microwave Photonics (MWP) 2012 , Norwijk, The Netherlands, paper Th5.5, 11-14 Sep. 2012.
G. Alcaro, D. Visani, G. Tartarini, L. Tarlazzi, P. Faccin,
“Controlling the impact of Modal Noise on Harmonic and Intermodulation distortions in Radio over Multimode Fiber links,”
36th European Conference and Exhibition on Optical Communication (ECOC) 2010 , Torino, Italy, paper We.7.B.5, 19-23 Sep. 2010.
D. Visani, G. Tartarini, M. N. Petersen, L. Tarlazzi, P. Faccin,
“Reducing Modal Noise in Short-Range Radio over Multimode Fibre Links,”
OSA Optical Fiber Communication Conference (OFC) 2010 , San Diego, CA, USA, paper JWA56, 21-15 Mar. 2010.
D. Visani, G. Tartarini, L. Tarlazzi, P. Faccin,
“Accurate and efficient transmission evaluation of wireless signals on radio over fiber links,”
IEEE International Topical Meeting on Microwave Photonics (MWP) 2009, Valencia, Spain, paper Th4.17, 14-16 Sep. 2009.
L. Rosa, D. Passaro, S. Selleri, G. Tartarini, P. Faccin, E.M. Fabbri,
“Simulation and Measurement of Intermodulation Induced by Chirp-Dispersion Interaction in Radio-over-Fiber Systems”
IASTED International Conference on Antennas, Radar and Wave Propagation ARP 2007. Montreal, Canada. May 30 - June 1, 2007
L. Rosa, S. Selleri, G. Tartarini, E. M. Fabbri, P. Faccin,
“Intermodulation Distortion Modelling in IM-DD Multi-Band Radio over Fibre Links”.
International Topical Meeting on Microwave Photonics (MWP 2006). Grenoble (F). 3-6 October 2006.
S. Selleri, L. Rosa, G. Tartarini, P. Faccin, E. Fabbri,
“Distortion Performance Prediction in Multi-band Radio over Fiber Systems Exploiting Direct Laser Modulation”
European Microwave Week 2006. Manchester (U.K.). 10-15 September 2006.
A. Faniuolo, G. Tartarini, P. Bassi, P. Faccin, A. Casini,
“Effects of directly modulated laser chirp on the performances of radio over fiber systems”
IEEE International Topical Meeting on Microwave Photonics (MWP) 2003 , Budapest, Hungary, pp. 283-286, 2003.

## Slide 26
Thanks!

## Slide 27: RoF link based on VCSEL
SFDRRXchain DFB = 91dB/Hz2/3
SFDRRXchain Copper =91.6dB/Hz2/3
SFDRRXchain = 90dB/Hz2/3
(SFDRLink(VCSEL)=104dB/Hz2/3)
500m link on MMF
SFDR (dB/Hz2/3) | 104
Gain (dB) | -29
NF (dB) | 39
OIP3 (dBm) | -8
RF Transmission Over Multimode Fibers Using VCSELs - Comparing Standard and High-Bandwidth Multimode Fibers.
C. Carlsson , A. Larsson, A. Apling.
IEEE Journal of Lightwave Technology, 2004.

## Slide 28: Current and future work
Comparison of VCSEL/MMF&SMF with DFB/SMF using:
  -BEST2: 32 elem. 2D, Ac=1400m2
  -BEST3-lo: 16 elem. 1D, Ac=800m2
VCSEL links for AAVS0